## Slide 1: Introduction to Electric and Electronics
Chapter 11 –
Analog Electronics

## Slide 2: Learning Objectives
Learning Objectives
To recognize the impact on society of transistors and integrated circuits
To gain a understanding of the basics of analog signals and circuits
To develop an understanding of how MOS and BJT transistors operate
To learn to analyze MOS and BJT analog circuits
To understand large-signal analysis with load lines, integrated with small signal analysis

## Slide 3: Introduction
Introduction
The functions of a transistor
  electronically controlled switch in digital circuits
  electronic amp in analog circuits
Types of transistors
  FET : field effect transistor, controls current by voltage
  BJT : bipolar junction transistor, controls current by voltage

## Slide 4: Introduction
Amplifiers
  Smaller-signal amplifiers
    voltage variations are reasonably small
    a few hundreds of millivolts
    can be approximated by linear circuit models
  Large-signal amplifiers
    voltage swings are large
    several volts or more
    used to provide high levels of signal output(stereo amp)
    similar to switching circuits

## Slide 5: MOSFET
MOSFET
MOSFET : metal-oxide-semiconductor FET
  most commonly used
  MOS transistor
Types of MOSFET
  n-channel and p-channel
  Enhancement mode and depletion mode

## Slide 6: MOSFET
MOSFET Structure and Symbols

## Slide 7: MOSFET
MOSFET Device Operation
iD : drain current
  current through S-D loop
  controlled by gate-to-source voltage VGS
VT : threshold voltage
  if VGS > VT, then iD>0

## Slide 8: MOSFET
Output characteristic curves
V-I curves of transistors
Given VGS, sweeping VDS, and output ID
IS = ID

## Slide 9: MOSFET
Regions of Operation
  ohmic region : ID rise with increasing VDS
  active or saturation region : ID remains almost constant with increasing VDS
  cutoff region : ID = 0, VGS < VT

## Slide 10: MOSFET
Drain current
ohmic region
Saturation region
Cutoff region

## Slide 11: MOSFET
Biasing Techniques
Lode line
Q-point

## Slide 12: MOSFET
Example 11.1
Determine Q-point

## Slide 13: MOSFET
The NOT Gate: MOSFET Implementation
NOT Gate(Inverter)
  Low input → High output
  High input → Low output
Load line
From load line

## Slide 14: MOSFET
Small-signal analysis of MODFET circuits

## Slide 15: MOSFET
Example 11.3
Find

## Slide 16: MOSFET
Common source amplifier

## Slide 17: MOSFET
Other FET Amplifier Configurations

## Slide 18: BJT
BJT(Bipolar Junction Transistor
BJT Structure
bipolar junction transistor
two p-n junction diodes fabricated very close
PNP transistor and NPN transistor
base (B) : center region of BJT
emitter (E) : emitting carriers
collector (C) : collecting carriers

## Slide 19: BJT
BJT Device operation
four possible bias conditions
  emitter junction
  collector junction
  cutoff or off : open switch
  on or saturated : closed switch

## Slide 20: BJT
BJT in the Active Region
two diodes are extremely close together
collect current exists even though the collector junction is reverse biased
Forward common base (CB) current transfer ratio

## Slide 21: BJT
BJT in the Active Region (continue)
Turn-on voltage
Emitter current
Collect current
Common emitter current gain

## Slide 22: BJT
Output characteristic curves
There are three regions in BJT output curves
  cut-off region, saturation region, active region

## Slide 23: BJT
Example 11.6 (Q-point)

## Slide 24: BJT
Small signal analysis
Equivalent Circuit

## Slide 25: BJT
Common Emitter (CE) Configuration
  ⇒
  CE configuration equivalent circuit
collector current
  here is forward CE current transfer ratio

## Slide 26: BJT
Other BJT Amp Configurations
BJT Circuit configuration

## Slide 27: Thyristors, SCRs and Motor Control
Thyristors, SCRs, and Motor Control
Thyristors and SCRs
  four layer structure (pnpn)
  Control large amount of power with only a small amount of control energy.

## Slide 28: Thyristors, SCRs and Motor Control
Thyristors
  Breakover voltage
SCRs
  Silicon-controlled rectifiers
  Control connection G

## Slide 29: Homework
Homework
Solve Problem 11.2, 11.4, 11.7, 11.28, 11.38
Prepare Final Exam.